## Slide 1
Hydrological
Module
Mikhail Smilovic
FUSE team meeting on June 8, 2020

## Slide 2: Outputs:
OUTPUTS
Evapotranspiration (land)
River
discharge
Channel evaporation
non-Irrigation consumption
Waterbody evaporation
Evapotranspiration on land is the dominant outflow from the watershed.
Highlight
Last time, we talked of the water balance. The main output from the Nira basin watershed is evapotranspiration on land, namely, water consumed by plants and evaporation from the soil and canopy.

## Slide 3
Irrigated
non-Irrigated
Sugarcane, variety pre-seasonal
Fraction of land planted
Fraction of land planted

## Slide 4
2.
Input for each crop / irrigation status
Irrigated
3.
On the first day of each month, crops that are finished growing are harvested. Then, if land is available, crops to be planted in this month are sown
non-Irrigated
1.
Input for total Irrigated land and non-irrigated land
non-Irrigated
Irrigated
Crop | Planting month | Growing length (months)
Sugar1 | July | 17
Sugar2 | October | 15
Sugar3 | January | 12
Sorghum | November | 4
Groundnut | June | 5
Wheat | November | 5
Maize | November | 5
4.
Each crop has four growth stages determining potential water use, determined by scaling a reference water use by crop- and growth-stage specific water use coefficients (Kc)
Chart: Water use coefficients (Kc), growth-stage specific
| Sugar1 | Sorghum | Groundnut | Wheat | Maize
KC1 | 0.4 | 0.7 | 0.45 | 0.45 | 0.45
KC2 | 0.8 | 0.925 | 0.75 | 0.75 | 0.75
KC3 | 1.25 | 1.15 | 0.95 | 0.95 | 0.95
KC4 | 0.75 | 0.55 | 0.75 | 0.75 | 0.75

## Slide 5
Irrigated
non-Irrigated
Fraction of land planted
Fraction of land planted
Sorghum

## Slide 6
Irrigated
Non-Irrigated
Sugarcane, v. pre-s
Sorghum

## Slide 7
Non-Irrigated
Irrigated
Sorghum
Sugarcane, v. pre-s
Groundnut
Wheat

## Slide 9
River discharge example year 2006

## Slide 10
Reservoirs example years 2005-06

## Slide 11
Groundwater

## Slide 13: Calibration parameters
Parameter | Value | Min | Max | Notes
Crop evapotranspiration factor | 9e-6 | 0.7 | 1.9 | 
Soil depth factor | 1.2 | 0.8 | 1.5 | 
Infiltration capacity | 0.4 | 0.01 | 1 | Empirical shape parameter b of the ARNO model
Interflow | 1.7 | 0.33 | 3 | Scales the amount of interflow going to channel storage and groundwater
Permeability (m/s) | 9e-6 | 5E-07 | 0.00001 | 0.0432 - 0.864 m/day
Porosity (specific yield) | 1.6% | 0.7% | 4% | 
River fraction factor | 0.9 | 0.5 | 2 | Scales fraction of rivers
Preferential flow factor | 7.8 | 0.5 | 8 | Empirical shape parameter of the preferential flow relation
Channel Manning’s n factor | 7.2 | 0.1 | 10 | Roughness factor in channel routing
Open water evaporation factor | 1.6 | 0.8 | 2 | 
Lake A factor | 1.2 | 0.333 | 3 | Scales channel width and weir coefficient as a part of the Poleni weir equation
Notes: Snowmelt coefficient in [m/C deg/day] as a degree-day factor
Recession coefficient factor: factor to adjust the base flow recession constant
Runoff concentration factor: a factor for the concentration time of run-off in each grid-cell
Normal storage limit: the fraction of storage capacity used as normal storage limit